## Slide 1
Light and Optics I
CS 498: Virtual Reality
UNIVERSITY OF ILLINOIS AT URBANA-CHAMPAIGN
Eric Shaffer

## Slide 2: Light and Optics
Why are they relevant to VR?
To build a headset, need to understand interaction between eye and display
Need to model transport of light in the virtual world
Optics are also used in
  Image acquisition (e.g. 360 degree cameras)
  Tracking

## Slide 3: Light Models
Three light models
Ray model: A ray traces the motion of a single hypothetical photon. Helpful when explaining lenses and defining the concept of visibility
Wave mode: Ripples through space that are similar to waves propagating on the surface of water. Helpful when considering spectrum of light.
Particle model: Tiny particles of energy moving through space at high speeds Helpful measuring the amount of light received by a sensor.
Point source of light
Light is light…it isn’t any of these but it behaves like all of them.

## Slide 4: Light Propagation
In the absence of lenses …or gravitational anomalies…light travels in straight lines
Can model a light as a point emitting photons in all directions
  Photons spread spherically …surface area of a sphere is 4πr2 …which implies the energy of light decreases quadratically with distance

## Slide 5: Light from Far Away…
Farther away a light source, the more the curvature of the wavefront flattens
For a light “infinitely” far away, the rays would become parallel
  Sunlight on earth is often modeled this way

## Slide 6: Light and Materials
Simple model of light/material interaction
Absorption
Reflection
Transmission

## Slide 7: Models of Reflection

## Slide 8: Visible Light is Usually a Jumble of Wavelengths
From Virtual Reality by LaValle
What do we call something emitting a single coherent wavelength of light?

## Slide 9: Lenses

## Slide 10: Snell’s Law
Describes how much light bends when entering or exiting a material
Refractive Index for a material is
C is speed of light in vacuum S is speed of light in material

## Slide 11: Snell’s Law

## Slide 12: Internal Reflection
Light is transmitted if
Otherwise, there is internal reflection

## Slide 13: Light through a Prism
Slope of prism determines direction light bent

## Slide 14: Simple Convex Lens Model
What is unrealistic about this model?

## Slide 15: Focus
Light will not be from infinitely far away Light will be reflected from different distances to lens
No single plane in which entirety of object is in focus

## Slide 16: Magnification
If object very close to lens
Lens cannot force its outgoing light rays to converge to a focal point.
In this case, lens works as a magnifying glass.
This is the way lenses are commonly used for VR headsets.

## Slide 17: Lensmaker’s Equation: Converging Lens
r1 and r2 are the radius of curvature of each of the two lens surfaces
also assumes a thin lens approximation, which means that the lens thickness is small relative to r1 and r2.
What are we interested in computing with this? What could it be used for?

## Slide 18: The Lensmaker’s Equation: Diverging Lens

## Slide 19: Convenient Unit: Diopter
Diopter is a converging (diverging) power of a lens.
D = 1 / f, (m-1)

## Slide 20: Combined Optical Power of a Chain of Lenses

## Slide 21: Problems with Lenses
Many issues have to be addressed to generate a high-quality image
Chromatic Aberration
Spherical Aberration
Optical Distortion
Astigmatism
Coma and Flare

## Slide 22: Chromatic Aberration
Different wavelengths of light
  Different speeds through media
  Causes divergence
  Can be fixed
    Multiple lenses of different media

## Slide 23: Spherical Aberration
Rays further from lens center refracted more
Fixes are possible…aspheric lens…complicated….

## Slide 24: Optical Distortion
Different from spherical aberration (which is blurring)
Image magnification increases or decreases with distance from the optical axis

## Slide 25: Coma and Flare
Off-axis point lights have tails or flare