## Slide 1
Tracking: Optical Techniques
CS 498VR: Virtual Reality
UNIVERSITY OF ILLINOIS AT URBANA-CHAMPAIGN
Eric Shaffer
Based on material from: Gordon Wetzstein, Stanford University

## Slide 2: Tracking Position and Orientation
Now we will discuss tracking all 6 DOFs for a moving rigid body
We call the position + orientation the pose
Why track? To map user movement into the virtual environment.

## Slide 3: Overview of Positional Tracking
“inside-out tracking”: camera or sensor is located on HMD, no need for other external devices to do tracking
simultaneous localization and mapping (SLAM)
computer & robotic vision problem (beyond this class)
“outside-in tracking”: external sensors, cameras, or markers are required (i.e. tracking constrained to specific area)
used by many slightly older HMDs (Rift and Vive)

## Slide 4: Integrate the Accelerometer?
We could subtract off acceleration due to gravity and find body acceleration…
What do we need to estimate position?
How does that contrast with using a gyroscope to compute orientation?
What is effect on the error?
Can the IMU sensors be used to correct positional drift error?

## Slide 5: Integrate the Accelerometer?
What do we need to estimate position? Integrate twice
How does that contrast with using a gyroscope to compute orientation? Only a single integration is necessary to find orientation from angular velocity
What is effect on the error? It’s significantly worse when integrating twice
Can the IMU sensors be used to correct positional drift error? No…can’t detect even constant velocity

## Slide 6: Active Tracking
Another approach is to create a signal to be sensed
Many approaches have been tried
Infrared
Ultrasound
Electromagnetic

## Slide 7: Trilateration
Consider something like ultrasound
Emitter is a speaker and detector is a microphone
Speaker emits at known time intervals…
Time of Flight (time to detection) enables computation of distance
Three emitters allow unique determination of location…

## Slide 8: Sound and EM…and Visibility
Both kinds of systems have been problematic
Sound reflects off objects in the rooms leading multiple detections
Environment can warp EM fields and thus warp detected trajectories
Visibility approaches have been more robust
Camera can be used to track features
Oculus Rift system tracks infrared LEDs on the HMD

## Slide 9: A Quick Guide to Features
Natural Features: Automatically discovered and labeled
Artificial Features: Engineered and placed in scene with assigned labels
Passive Features: Do not emit energy…can reflect energy (i.e. light)
Active Features: Emit light

## Slide 10: Perspective-n-Point Problem (PnP)
Using n-points on an object in an image, compute the pose matrix Trb
Each observed point (i,j) in image coordinates eliminates 2 DOFs
For 3 points (i.e. P3P) 0 DOFs remain but solution is not unique
P6P required for unique solution
More than 6 points generally used to make solution robust to error
Remember: We are computing the pose of the camera

## Slide 11: Positional Tracking - Optical
track active (near IR) LEDs with cameras
OR
track passive retro-reflectors with IR illumination around camera
both Oculus Rift and HTC Vive come with optical tracking
Oculus Rift
https://www.ifixit.com/Teardown/
Oculus+Rift+CV1+Teardown/60612

## Slide 12: HTC Lighthouse
Lighthouse HTC Vive tracking is an example
Lighthouse has spinning drum emitting vertical and horizontal IR light
Photodiodes on HMD detect IR light

## Slide 13: HTC Lighthouse

## Slide 14: HTC Lighthouse
Bright IR flash followed by 2 sweeps of IR light
Horizontal light determines column of feature coordinate
Vertical light determines row of feature coordinates Time delay from flash reflection to sweep reflection is recorded by HMD photodiodes
Multiple base stations needed to compute distance from feature to station

## Slide 15: Example: HTC Lighthouse

## Slide 16: Understanding Pose Estimation
2D
projections
Estimating 6-DoF pose from 2D projections is known as the
Perspective-n-point problem!
For pose estimation, need to track multiple points with known relative 3D coordinates

## Slide 17: Image Formation
Map 3D points in object coordinate system to 2D points in window coordinates
With the Vive Lighthouse, the IR light sweeps allow the Vive to generate 2D “image points” associated with each photodiode on the Vive…

## Slide 18: Finding Pose: Use a Familiar Camera Model

## Slide 19: The Homography Matrix
In a very constrained case, we can simplify the model to be as you see above
We assume all the marker points are co-planar and at z=0 in the local frame.
We want to find the Homography matrix H…that will ultimately give us a pose

## Slide 20: Finding Pose: Linear Homography Method
Homography matrix has 8 degrees of freedom
Any scaled version of the matrix can be used…get the same result

## Slide 21: Scaling the Homography Matrix
So…estimate a scaled version of the matrix where h9 = 1

## Slide 22: Image Formation with Scaled Matrix

## Slide 23: Reorganize the Equation

## Slide 24: Need a System of Equations

## Slide 25: Use 4 Marker Points...Solve System

## Slide 26: Need to Find Scale….

## Slide 27: Compute the Position

## Slide 28: Get Rotation

## Slide 29: Temporal Filter to Smooth Noise
 , , ,t ,t ,t
x y z x y z
filtered
( k )
   , , ,t ,t ,t
x y z x y z
   
filtered
1
k 
 
 1   
, , ,t ,t ,t
x y z x y z
 
unfiltered
k 
pose estimation is very sensitive to noise in the measured 2D coordinates!
 estimated position and especially rotation may be noisy
apply a simple temporal filter with weight  to smooth the pose at time step k:
smaller   less filtering, larger   more smoothing

## Slide 30: Inside-Out Tracking

## Slide 31: Oculus Quest